## Slide 1: Project Planning for Weavers
Sandi Petty
Judy Mooers
Jan. 18, 2010

## Slide 2: Where do We Start
What am I going to weave?
What yarn should I use?
How much yarn do I need?
Sample or weave
Evaluation and documentation

## Slide 3: Sizes for Some Common Products
Table Linens
  Napkins, casual: 12” x 12”
  Napkins, formal: 16” x 16”
  Placemats, casual: 12” x 18”
  Placemats, formal: 14” x 20”
Kitchen
  Dish towels: 15” x 20”
  Dishcloths: 10” x 10”
  Pot holders: 7” x 7”
  Tea towels: 16” x 28 “ (small)
  Tea towels: 24” x 34” (large)
Bathroom
  Washcloth: 14 “ x 14”
  Hand towel: 16” x 28”
  Bath towel: 22” x 24” (sm)
  Bath towel: 24” x 46” (med)
  Bath sheet: 36” x 70”
Apparel
  Men’s formal scarf: 12” x 45”
  Women’s formal scarf: 10” x 48”
  Women’s shawl: 24” x 72”
  Baby Blanket: 36” or 45” square

## Slide 4: Choosing the Yarn
The Fiber
  Softness
  Washability
  Durability
The Yarn
  Strength (for warp)
  Grist
  Structure
  Size

## Slide 5: Fiber Properties
 | Wool | Silk | Linen | Cotton | Rayon
Absorbency (water as fraction of weight) | Good | Good | Excellent (evaporates readily) | Excellent (evaporates slower than linen) | Good
Elasticity | High (can stretch 30%) | Good, but less than wool | Very low | Low | Moderate
Strength | Weak (especially wet) | Very strong (less when wet) | Very strong (especially wet) | Moderate (more when wet, mercerized stronger) | Low
Warmth | Good | Very Good | Low | Moderate | Moderate
Ease of Cleaning | Avoid agitation | Requires care | Very good | Good | Moderate
Weaver’s Companion, pg. 25-27.

## Slide 6: Setts for Some Common Yarn Styles
Yarn Type | Yards per Pound | Plain Weave | 2/2 Twill
20/2 Cotton | 8400 | 24 - 30 | 32 - 36
10/2 Cotton | 4200 | 24 - 28 | 30 - 32
8/2 Cotton | 3000 | 16 - 20 | 24 - 30
5/2 Cotton | 2100 | 15 - 18 | 20
3/2 Cotton | 1260 | 10 - 12 | 15
20/1 Linen | 6000 | 24 - 30 | 36 - 40
12/1 Linen | 3600 | 22 - 25 | 30 - 32
20/2 Linen | 3000 | 20 - 24 | 24 - 30
30/2 Silk | 7500 | 30 - 32 | 36 - 45
12/2 Silk | 3000 | 18 - 20 | 22 - 24
20/2 Wool | 5600 | 20 - 24 | 30 - 36
12/2 Wool | 3000 | 18 - 20 | 22 - 25
6/2 Wool | 1600 | 10 - 12 | 12 - 15

## Slide 7: Determining Sett (Ends per Inch or epi)
Wind the warp around a ruler for one inch
  Firm, even, no stretch
  Fill the space with no overlap
  Count for wraps/inch = W (warp yarn diameter)
Weft yarn diameter = F
  Calculate same as above
Eileen Hallman

## Slide 8: Determining Sett (Ends per Inch or epi) continued
Number of threads in one repeat of the weave structure = T
(plain weave (1,2)= 2; twill weave (1,2,3,4)= 4
Number of intersections in one repeat of the weave structure = I
(plain weave = 2; twill weave = 2)
Sett = (T x W x F) / ( T x F + I x W)
Eileen Hallman

## Slide 9: Formula for Sett
S = (T x W)/ (T + I)
  S = sett
  T= number of ends in one repeat of the threading
  W = yarn diameter or wraps/inch
  I = number of interactions that the weft has with the yarn in one repeat
Manual of Swedish Weaving

## Slide 10: Warp Ends Calculation All Measurements in Inches
Final Planned Width | 
+ Take-up (e.g., 10%) | 
+ Shrinkage (e.g. 10%) | 
= Width on the loom | 
x ends per inch (epi) | 
= Warp ends | 
+/- Adjustment for pattern | 
Marcy Petrini

## Slide 11: Warp Length Calculation All Numbers in Inches
Final Length, include hem | 
+ Shrinkage (10%) | 
= Length to weave | 
+ Fringe | 
+ Take-up (10%) | 
= Length per article | 
x number of articles | 
= Warp length for weaving | 
+ Loom waste (18” to 27”) | 
= Total warp length (inches) | 
Total warp length (yards) (divide by 36) | 
Marcy Petrini

## Slide 12: Amount of Yarn Needed
Yarn for warp
Yarn for weft
Total ends to wind | 
x Length of each warp thread (yds) | 
= Total warp needed (yards) | 
= Total warp needed (pounds) (Divide by yards/pound) | 
Width on the loom (inches) | 
x Beat (picks per inch) | 
x Warp length for weaving | 
= Total weft needed (inches) | 
= Total weft needed in yards | 
= Total weft needed in pounds | 
Marci Petrini

## Slide 13: Determining Yardage
Count system for yardage
Number of yards in a pound of a “standard” yarn
  Cotton and spun silk: 840
  Linen, hemp, jute, ramie: 300
  Worsted wool: 560
  Woolen wool: 256
Yardage of a single= count x the standard
Yardage of a plied yarn= yardage of single/# of plies
Weaver’s Companion, pg. 30

## Slide 14: Sources for Yards per pound
Yarn supplier
Weavers Companion
Handwoven Magazine – yarn and suppliers page in any issue

## Slide 15: Reed Size Table
Reed # | 1,0 | 1 | 1,2 | 2 | 2,3 | 3 | 4
6 | 3 | 6 | 9 | 12 | 15 | 18 | 24
7 | 3.5 | 7 | 10.5 | 14 | 17.5 | 21 | 28
8 | 4 | 8 | 12 | 16 | 20 | 24 | 32
9 | 4.5 | 9 | 13.5 | 18 | 22.5 | 27 | 36
10 | 5 | 10 | 15 | 20 | 25 | 30 | 40
11 | 5.5 | 11 | 16.5 | 22 | 27.5 | 33 | 44
12 | 6 | 12 | 18 | 24 | 30 | 36 | 48
14 | 7 | 14 | 21 | 28 | 35 | 42 | 56
15 | 7.5 | 15 | 22.5 | 30 | 37.5 | 45 | 60
16 | 8 | 16 | 24 | 32 | 40 | 48 | 64
18 | 9 | 18 | 27 | 36 | 45 | 54 | 72
20 | 10 | 20 | 30 | 40 | 50 | 60 | 80
Mary Black, pg. 659

## Slide 16: Sampling
Purpose: check sett, ppi, structure, shrinkage, flaws in the yarn, effects of color and texture, finishing techniques, and fabric hand.
Make each sample at least 6-10” wide and long. Sample warp should be long enough to re-sley and re-tie (e.g., 2 yards)
Record length and width
  On the loom
  Off the loom
  Finished

## Slide 17: Project Notes
Name of project _________________________
Date completed _________________________
Approx. time req’d _______________________
Yarns: Warp ___________Weft____________
Weave Structure ________________________
Source ________________________________
Warp length ___________________________
Warp width ____________________________
Sett __________________________________
PPI ___________________________________
Dimensions on loom _____________________
Dimensions off loom _____________________
Dimensions after finishing _________________
Insert draft
Weaver’s Companion, pg. 41

## Slide 18: References
The Weaver’s Companion, Interweave Press: Loveland, CO, 2001, pp. 25-42.
“Right from the Start: Planning a Project”, Marcy Petrini, http://www.weavespindye.org/pages/rfts-doc.html.
“Right from the Start: Planning a Project”, Shuttle, Spindle & Dyepot, 122(Spring 2000),45-48
“The Whole Truth about Setts”, Eileen Hallman, Weavers, 40(1998), 18.
Learning to Weave, Deborah Chandler, Interweave Press: Loveland, CO 1995, pp. 103-110.
The Big Book of Weaving, Laila Lundell, Trafalgar Square: North Pomfret, VT, 2005, pp. 11, 88-93.
The Key to Weaving (2nd revised edition), Mary Black,Macmillan Publishing Co.: New York, NY, 1980, pp. 14-16, 657- 662.